NMRA-DCC
NMRA-DCC
Selfmade Decoder Projects
based on PIC12CE519 and Attiny15
FREMO JT 2002 Enschede

---
PowerPoint-Präsentation
Structure
Throttle
LocoNet
Central
Unit
Booster
Loco with Decoder
Rail

---
Agenda
Agenda
- Technical Background
- Processor
- Simulator
- First outcome
- Decoder Projects
- Electronic Parts

---
Technical Background
Technical Background

---
Signal Shape
Signal Shape
Command control signal shape:
  - Right angled wave form
  - min. +/- 7 Volt
  - max. +/- 22 Volt
  - Transitions between - 4 Volt and + 4 Volt
    shall occure 2,5 Volt / µs or faster
  - Ripple at zero-crossing not under 100 kHz
    and no more than one fifth of the total amplitude
Voltage resistivity for Decoder:
  - min. +/- 24 Volt for „N“ scale and smaller
  - min. +/- 27 Volt for scale larger than „N“

---
Timing
Timing
Invert the rail power in fixed time slices and symmetric to voltage levels that have opposite polarity
„positiv“ signal equal to „negativ“ signal
except: stretched 0 bit to drive one analog loco on digital track
Fixed time slice:
 Zentral station	Decoder
1 = 55 - 61 µs	1 = 52 - 64 µs
0 = 95 - 9900 µs	0 = 90 - 10000 µs
With this timing the Decoder must read the bits in every situation.

---
Data Transmitting
Data Transmitting
- Preample minimum 10 times „1“
- 0 split data packet
- 1. Byte (8bit)
- 0 split data packet
- n. Byte (8bit)
- 0 split data packet
- EXOR over all bytes for error detection
- 1 end of data packet

---
Data Format for Loco Decoder
Data Format for Loco Decoder
- 0AAA AAAA	short Address
- 11AA AAAA & AAAA AAAA	long Address
- [Address] 01DL SSSS [EXOR] Direction Light & 14 Speed
  Light bit used for lowest 28 Speed step
- [Address] 0011 1111 & DSSS SSSS [EXOR]	126 Speed
- [Address] 100L FFFF [EXOR]	Light & Function 1 - 4
- [Address] 1011 FFFF [EXOR]	Function 5 - 8
- 0000 0000	Broadcast Address for all Loco Decoder
- 1111 1111 & 0000 0000	Idle Packet for all Decoder

---
Data Format for Accessory Decoder
Data Format for Accessory Decoder
10AA AAAA & 1AAA CDDD
9 Bit Accessory on/off F1-F8
1011 1111 & 1000 CDDD
Broadcast Command for all Accessory Decoder
1111 1111 & 0000 0000	Idle Packet for all Decoder

---
Programming Modes
Programming Modes
REG	Register	3 Bytes
Only CV1-CV8 reachable
PAG	Paged	2*3 Bytes
Slowly readout of CV‘s
All 1024 CV‘s in 16 by 64 pages
DIR	Direct	4 Bytes
fast readout of CV‘s
All 1024 CV‘s direct programmable
POM	Programming on main	5-6 Bytes
Programming on main track, no acknowledge
all 1024 CV‘s in real access reprogrammable

---
14 / 28 Speed Step
14 / 28 Speed Step
[Address] 01DL SSSS [EXOR] Direction Light & 14 Speed
        0 4 3 2 1	Direction & 28 Speed
14 Speed steps	28 Speed steps
0000 = Stop	00000
00001
0001 = Estop	00010
00011
....	....
1111	11111

---
128 Speed Step
128 Speed Step
128 Speed Step
[Address] 0011 1111 & DSSS SSSS [EXOR]
  Direction & 126 Speed steps
128 Speed steps
0000000 = Stop
0000001 = Estop
....
1111111

---
Processor
Processor

---
PIC12CE519
PIC12CE519
l
On-chip Oscillator
1 Timer
2 HW stack
33 Instruction
16 Byte EEPROM
1k*12 PROM
1024 prog steps

---
ATtiny15
ATtiny15
On-chip Oscillator
Ext. Interrupt
2 Timer
Hardware PWM
ADC
Anlog Comparator
90 Instruction
Watch Dog
Brown-Out
64 Byte EEPROM
1k Flash ROM
512 prog steps

---
Simulator
Simulator

---
Microchip MPLAB IDE
Microchip MPLAB IDE

---
Atmel     AVR Studio
Atmel AVR Studio

---
First outcom
First outcom
Extract accessory DCC commands from Arnold Control 80 with 10 MHz analog oscilloscope
Build decoder for pointing motor and stepper with fixed address based on PIC12C509

---
Decoder Projects
Decoder Projects
Stepper
Accessory Decoder
Iron Core Decoder (PWM ~90Hz)
Can Decoder (PWM >16kHz)

---
Detect „1“ with 44µs time loop  Full Bit Detection
Detect „1“ with 44µs time loop
Full Bit Detection
min. 52µs
1 2 3 1 2 1 2 3
1 2 3 1 2 3 1 2
time loop 44µs
max. 64µs
0 or 1 = frame error
2 or 3 = 1
    > 3 = 0
[Speaker Notes: The timing of 1 bit is fixed at 52-64µs. If we poll the port with 44µs time loop, then a „1“ is represented by 2 or 3 times read positive _and_ negative part of bit. Greater than 3 represent a zero (timing >90µs) and 0 or 1 is a frame error. With full bit detection, we need to detect the polarity of the bit stream.]

---
Detect Polarity
Detect Polarity
1
0
pos
Low
Hi
1
0
0
1
neg
pos
Hi
Low
1
0
neg = POL = 1
pos = POL = 0
[Speaker Notes: The polarity of the DCC signal can be detected by the change of the bits.]

---
Decode  Packet
Decode
Packet
Preample
CALL
ok
= 0
PRE-1
INLO
PRETEST
> 0
< 4
HI = 1
HI+LO
LO = 0
BIT=1
>= 4
BIT=0
< 4
HI+LO
BYTE
BIT=1
HI = 0
LO = 0
INTEST
>= 4
PRE = 9
BIT=0
INCF FSR
BIT=0
no Preample
Next Byte
>= 4
CALL
= 0
HI+LO
PRE-1
INLO
HI = 0
< 4
> 0
LO = 0
Next Bit
BIT=1
PRE = 11
FSR = PRE
EXOR
HI = 1
RLF INDF
LO = 0
[Speaker Notes: You can find the words written in grey in the diagram in my source code as jump mark. The yellow part wait for a preample. Then pretest waits for „0“ to begin to read the first byte. Set the indirect register to the first byte and read bit by bit 8 times. If the 9th bit is „0“ then read in next byte. If the 9th bit is „1“ then jump to EXOR.]

---
Polling Port
Polling
Port
0
INLO
POL
1
1
0
GP3
0
1
>0
LO
RETURN
GP3
LO +1
0
IST
CALL
HI +1
INLO
INHI
SPDTAB
STEP
Z1LOG
>0
Soll
IST
0
Stop
Z2TAB
1
Soll
Z1=0
Z2LOG
EStop
>1
[Speaker Notes: Full bit detection. Poll input port every 44µs, count up LO and HI counter. Exchange speedtables and set counter Z1 to zero if stop or estop detect.]

---
Principe of Stepper
Principe of Stepper
1
2
4
3
N
     S
N
     S
N
     S
N
     S
[Speaker Notes: The change of the polarity of one coil moves the magnet 90°]

---
Calculate Steps
Calculate
Steps
0
STEP
Z1-1
Z1=Z1LOG
<>0
ISO
B
F
DIR
0
1
0
1
S1
S0
0
1
0
1
S0
S0
S1
S1
0
1
0
1
S1=1
S0=0
S0=1
S1=0
S0=1
S1=0
S1=1
S0=0
RETURN
[Speaker Notes: The step routine will be executed after Z1LOG*44µs (Z1-1) Copy the actual speed for the stepper (Z1LOG) into the counter (Z1) Check direction Check the polarity of the stepper coils and change the polarity of the coil to bring the stepper to rotate to that direction]

---
Compare Speed
Compare
Speed
ISO
INC
<>0
<>0
Z2-1
TMR
0
0
Z1 +1
TMR=DELAY
Z2=Z2LOG
pos
neg
1
IST-SOLL
FUNC,7
Z2 *2
IST -1
IST +1
0
0
RETURN
RETURN
[Speaker Notes: If timer=zero then copy value delay into timer and check speed to go with actual speed. Increase speed if result is positiv. Decrease speed if result is negativ. If timer <> zero then make a second loop to increase the stepping time.]

---
Pulse Width Modulation
Pulse Width Modulation
ON
OFF
0
44
255
ON
OFF
0
210
255
[Speaker Notes: Set port on and wait for the match of actual speed and timer value, then clear port.]

---
PWM (~ 90Hz)
PWM (~ 90Hz)
INC
PWM-1
TMR
<>0
0
M1=0
M2=0
0
<>0
IST-
SOLL
MOTOR
DIR
<
>
F
B
PWM
-IST
PWM
-IST
0
<=
>
<=
>
M1=1
M1=0
M2=1
M2=0
RETURN
IST+1
TMR=INC
IST-1
TMR=DEC
STEP
[Speaker Notes: To produce a PWM fittable to the polling port method, a PWM approx. 90Hz is the result.]

---
Detect „1“ with 22µs time loop Half Bit Detection
Detect „1“ with 22µs time loop
Half Bit Detection
min. 52µs
1 2 3 x x 1 2 3 x x 1 2 x x x
1 2 3 x x x 1 2 3 x x x 1 2 3
time loop 22µs
max. 64µs
0 or 1 = frame error
2 or 3 = 1
    > 3 = 0
[Speaker Notes: With half bit detection I can dismiss the polarity detection and save some ROM space.]

---
Increase speed of PIC
Increase speed of PIC
1
26(29), lock
Set OSCCAL to 0 and increment time loop,
test if „time loop“+1 fits into „1“ signal of DCC
- Information about OSCCAL register in data sheet from Microchip is wrong!
- Don‘t trust descriptions, see for yourself
[Speaker Notes: The time loop for the iron-core version is 25µs long and I found no way to produce a loop with 22µs, therefore I increase the speed of the PIC.]

---
18 kHz PWM with 28 Speed Step
18 kHz PWM with 28 Speed Step
9
2
11
9
9
9
27
Coarse
Block 1
9
9
10
Coarse
Block 2
Fine Block
1 2 3 4 5 6 7 8 9
9
9
2
2
9
9
18
20
9
2
9
Speed
[Speaker Notes: With the calibration method it is also possible to calibrate to 28µs time loop and I write a program for can motors with 18kHz PWM.]

---
One speed step = 2µs (~18kHz)
One speed step = 2µs (~18kHz)
MOVF	PWM_ON,0	; Fine Block	6
MOVWF	tmr0	;	7
MOVF	PWM,0	;(tmr0)	PWM	PWM1	PWM2	8
BTFSC	tmr0,3	;	9
MOVWF	GPIO	;(08)	9	18	19	10
BTFSC	tmr0,3	;	11
MOVWF	GPIO	;(07)	8	17	20	12
BTFSC	tmr0,3	;	13
MOVWF	GPIO	;(06)	7	16	21	14
BTFSC	tmr0,3	;	15
MOVWF	GPIO	;(05)	6	15	22	16
BTFSC	tmr0,3	;	17
MOVWF	GPIO	;(04)	5	14	23	18
BTFSC	tmr0,3	;	19
MOVWF	GPIO	;(03)	4	13	24	20
BTFSC	tmr0,3	;	21
MOVWF	GPIO	;(02)	3	12	25	22
BTFSC	tmr0,3	;	23
MOVWF	GPIO	;(01)	2	11	26	24
BTFSC	tmr0,3	;	25
MOVWF	GPIO	;(00)	1	10	27	26
MOVF	PWM1,0	;	27
MOVWF	GPIO	; Coarse Block 1	XX	XX	28
MOVF	PWM2,0	;	45
MOVWF	GPIO	; Coarse Block 2	XX	46
[Speaker Notes: Right hand you can see the time steps. Set the timer to the fastest speed. Copy PWM_ON into output port depend on the timer value. Switch off the output port with PWM1 or PWM2. The black and blue lines are together, the two red lines stand on position 45/46. The rest is done by the gaps between the PWM. The steps go to 56 and begin new at 1.]

---
Check Packet
Check Packet
CV
SHORTA
Short
Adress
EXOR
Bytes
B1=0
0
Y
Y
INDR=B2
<>0
N
N
START
B1=CV17
B2=CV18
CV29.5=1
CV19=0
B1=CV1
CV29.5=0
CV19=0
N
N
N
B1=
CV19
Y
B1>
119
Y
Y
N
Y
Long Adress
DECODE
PROG
INDR=B3
EXOR
CHKPROG
Broadcast
Consist
Short Adr
[Speaker Notes: If a packet is read then check it with exor over all bytes and branch. Set the indirect register to byte 3 if long adress is detected. If short adress then set indirect register to 2nd byte.]

---
Decode Packet
Decode Packet
DECODE
Y
INDF.654
INDR +1
Consist
Reset
Y
N
CV19
=BT3
CONCON
Reset
000 DECCON
001 ADVAN
010 FORWARD
011 REVERSE
100 FTION
101 FTION1
110 TELNEW
111
N
SOLL=
INDF*9
DIR=0
DIR=1
ASPEED
F1-F4
DIR=INDF.7
SOLL=INDF*2
F5-F8
CV49->GP2
CV50->GP4
CV51->GP5
B1=
CV1
B2=
Oack
Y
N
START
N
Y
Prog OTM
ACKNOW
[Speaker Notes: If a adress match then decode the data of the packet. ADVAN is the 126 speed step mode and FORWARD/REVERSE is the 14/28 speed steps.]

---
Mapping of CV49/50/51
Mapping of CV49/50/51
F1-F8
F1-F8
=CV50
CV64.0
F1-F8
=CV50
1
0
N
N
Y
Y
GP4=0
GP4=1
GP4&5=1
GP4&5=0
F1-F8
=CV51
CV64.1
F1-F8
=CV51
N
1
0
N
RLt=0
Use CV5
Y
Y
RLt=1
Use CV55
F1-F8
=CV49
N
Y
GP2=0
GP2=1
START

---
Write CV
Write CV
PROGREG
3Byte
=CV
Y
Y
PROG
EEPROG
N
N
Write CV
PROGOTM
=CV
N
Prog OTM
START
Xch Bit
Y
Y
BITMAN
WRITE
BIT
MAN
Y
N
N
N
N
EEVERI
EEPROG
WRITE
Byte
=CV
Bit
=CV
Y
N
Y
Y
Write CV
ACKNOW

---
Configuration Variables Selfmade Decoder Ironcore 22v10
Configuration Variables
Selfmade Decoder Ironcore 22v10
       cv1	Short Addresse
       cv2	Vstart
       cv3	Acceleration
       cv4	Deceleration
       cv5	Vmax
       cv6	Vmid
cv17/18	Long Address
cv19	Consist Address
cv29	Config
cv49	F1-F8 -> GP2
cv50	F1-F8 -> GP4
cv51	F1-F8 -> GP5
cv55	2. Vmax
cv64	Config 2

---
cv 6 Vmid Selfmade Decoder Ironcore 22v10
cv 6 Vmid Selfmade Decoder Ironcore 22v10
Speed Curve (CV6=30)
Subtraction Factor

---
cv 6 Vmid Selfmade Decoder Ironcore 22v10
Speed Curve (CV6=220)
Addition Factor

---
cv 29 Selfmade Decoder Ironcore 22v10
cv 29 Selfmade Decoder Ironcore 22v10
- 0	Flip direction with light
- 1	Light in 14 ss mode or in function group 1
  - 28 Speed Step auto detect
- 2	Light inverted (Analog mode)
- 3	(Advanced Acknowledge)
- 4	Internal speed table / cv2, cv5 & cv6
- 5	short / long Address
- 7	(Accessory Decoder)

---
cv 64 Selfmade Decoder Ironcore 22v10
cv 64 Selfmade Decoder Ironcore 22v10
0	F1-F8 defined in cv50 switches:
  - 0 = Rangierlicht – front light on both sides
  - 1 = Front light (GP4)
1	F1-F8 defined in cv51 switches:
  - 0 = 2. Vmax
  - 1 = Rear light (GP5)
- 2	Rear light
- 3	Brake light	(head light with function decoder)
- 5	Flickering fire box (switchable over cv49)
- 7	Autom. flickering fire box over drive speed

---
Connection Diagram without brownout
Connection Diagram
without brownout

---
Accessory Decoder
Accessory Decoder
5 Output Ports
Address and timer for every port pre definable
Simple programming of every port
ON time programmable with POM mode
Constant output
Mutuality between GP0/GP1/GP2 & GP4/GP5

---
Electronic Parts
Electronic Parts
12CE519	Microprocessor
ATtiny15	Microprocessor
si9986	1A so8 H-bridge
tle4207	0.8A so14 H-bridge
L272D	1A so16 Opamp
FDC6561AN	N-channel dual mosfet
FDC6506P	P-channel dual mosfet
S380 / MB6S	Rectifier

---
Where to get Electronic Parts
Where to get Electronic Parts
Andreas Bergmann	a.bergmann@electronic-design.com
Joachim Katzer	http://home.tiscalinet.de/jkatzer/
Bürklin	http://www.buerklin.com/
Conrad Electronic	http://www.conrad.de/
Future Electronics	http://www.futureelectronics.com/
Ineltec	http://www.ineltec.de/
Insight	http://www.insight.de.memec.com/
Mütron	http://www.muetron.de/
Reichelt	http://www.reichelt.de/
RS-Components	http://www.rs-components.de/
Spoerle	http://www.spoerle.de/